## Slide 1: AI-Based Power Factor Pattern Analysis and Classification
Capstone 9 | Electrical and Electronics Engineering

## Slide 2: Problem & Objectives
Analyze voltage, current, active power, reactive power, and power factor.
Clean simulated readings and investigate patterns over time.
Classify operating intervals as Low, Moderate, or Good PF.
Present trends and flagged intervals in a Streamlit dashboard.

## Slide 3: Electrical Theory
Single-phase approximation: apparent power S = V × I.
Power factor PF = P / S = P/(V × I).
Synthetic reactive power: Q = √(S² − P²).
Project bands: Low < 0.80; Moderate 0.80–<0.90; Good ≥ 0.90.

## Slide 4: Dataset & Preprocessing
6,003 simulated rows at 15-minute intervals.
Features include V, I, P, Q, load level, hour, and day of week.
Demonstration defects: duplicate rows and a few missing sensor values.
Remove duplicates, impute missing features, recalculate PF, assign labels.

## Slide 5: Machine Learning Method
Model: Random Forest classifier.
80% training / 20% held-out test split; stratified by class.
Median imputation is fitted within the training pipeline.
PF itself is excluded from features to avoid direct target leakage.

## Slide 6: Evaluation
Held-out accuracy: 0.938.
Review precision, recall, F1-score, and the confusion matrix.
Metrics describe performance on synthetic data only.
Validate on authorized real readings before making real-world claims.

## Slide 7: Dashboard
Date and PF-class filters.
PF and active/reactive power trends.
Class distribution and flagged intervals.
Sample classifier and CSV export.

## Slide 8: Limitations & Safety
Synthetic data can encode unrealistic patterns.
Power factor should be measured/calculated when reliable quantities exist.
Single-phase formulas do not automatically apply to three-phase systems.
No mains-connected compensation hardware; any compensation analysis remains simulation-only.

## Slide 9: Conclusion & Next Steps
End-to-end pipeline demonstrates EDA, preprocessing, ML, evaluation, and visualization.
Compare against simpler baselines and use time-aware validation.
Collect calibrated, authorized data for external validation.
Explain thresholds, assumptions, metrics, and limitations in the viva.